Enter the title of the presentation here
Cypress FX3 firmware
for INI Sensors
Luca Longinotti <luca.longinotti@uzh.ch>

---
Table of Contents
Overview
  - USB 3.0
  - Cypress FX3
  - FX3 SDK + Tools
  - FX3 Firmware
  - FX3 jAER integration

---
USB 3.0
  1. Since end of 2008, but spread started only 2011-2012
  2. More bandwidth: Super Speed 5Gbit/s
  3. Better power management: new power states (U0 to U3)
  4. New features: Bursts, Streams, …
    1. Asynchronous notifications
    2. Traffic only to target device
  5. Dual Bus Architecture: everything is supported!

---
USB 3.0 (2)
  - Electrically different, six new wires!
  - Backwards compatible to USB 2.0
    by also having the old wiring
  1. XHCI (eXtensible Host Controller Interface)
  2. Drivers from Host Controller vendors for Windows 7, (XP)
  3. Integrated driver starting with Windows 8
  4. Linux >= 2.6.31, Mac OS X >= 10.8

---
Cypress FX3
  - Supports USB 3.0
  - Up to 32 endpoints (16 IN, 16 OUT)
  - 32-bit, 200 MHz ARM CPU, 512 KB SRAM
  1. Boot from USB, I2C, SPI, GPIF2 ( + support for I2S, UART)
  2. GPIF2: 100 MHz operation, 8/16/32-bit data bus
  3. DMA-Engine
  4. ThreadX RTOS

---
FX3 SDK + Tools
  - Eclipse + GCC for ARM-based !!!
  - Various tools: GPIF2 Designer, ControlCenter
  - Easy install & automatic updates
  - Lots of examples
  - Good documentation
  - Well defined API Library

---
FX3 SDK + Tools: API Library
FX2:
EP0BUF[0] = SETUPDAT[1];
EP0BUF[1]= TIMESTAMP_MASTER; // PC1 (Port C Pin 1)
EP0BCH = 0;
EP0BCL = 2;
EP0CS |= bmHSNAK;
FX3:
uint8_t Buffer[2];
Buffer[0] = bRequest;
CyU3PGpioGetValue(GPIO_ID, &Buffer[1]); // GPIO Pin
CyU3PUsbSendEP0Data(2, &Buffer);

---
FX3 Firmware: FX2 Analysis
  - FX2 firmware: heavy fragmentation!
    - Different names, ports, …
    - But everyone kinda does the same!

---
FX3 Firmware: Framework
  - Solution: one framework, common core,
    additional features as options
    → Configurations for each device!
#define GPIF_32BIT_SUPPORT_ENABLED 0
#define I2C_SUPPORT_ENABLED 1
#define SPI_SUPPORT_ENABLED 1
#define GPIO_SUPPORT_ENABLED 1
gpioConfig_DeviceSpecific_Type cfg[] = {
  { 26, 'I'}, // GPIO 26 is an IN
  { 27, 'P'}, // GPIO 27 is an IN, and
  will interrupt on POS_EDGE ('N' NEG_EDGE,
  'B' BOTH_EDGES, 'L' LOW, 'H' HIGH)
  { 28, 'O'}, // GPIO 28 is an OUT
  { 45, 'E'} // GPIO 45 is a LED
};

---
FX3 Firmware: Features
  - Core: 16-bit GPIF Slave FIFO interface (Data EP2),
    USB debugging (Status EP1), default Vendor Requests (Control EP0),
    Heartbeat functionality (status messages, flashing LEDs, ...)
  - Optional:
    - 32-bit GPIF Slave FIFO interface
    - MS Feature Descriptor (WCID, WinUSB)
    - I2C support (EEPROM access or commands)
    - SPI support (Flash access or commands)
    - GPIO (configurable pins, IN/OUT, debug LED, …)
    - Device-specific initialization (load data from flash, ...)
    - DMA callbacks for Data EP2 to process/manipulate data

---
FX3 Firmware: Features (2)
  - Implemented default Vendor Requests:
VR_TEST	VR_LOG_LEVEL
VR_FX3_RESET	VR_STATUS
VR_SUPPORTED	(ON, OFF, TOGGLE, TIMED, RECURRING)
VR_GPIO_GET	VR_GPIO_SET
VR_I2C_CONFIG	VR_I2C_TRANSFER
VR_SPI_CONFIG	VR_SPI_CMD
VR_SPI_TRANSFER	VR_SPI_ERASE
  1. Can define device-specific Vendor Requests (override default)
CyBool_t CyFxHandleCustomVR_DeviceSpecific(
  uint8_t bDirection, uint8_t bRequest,
  uint16_t wValue, uint16_t wIndex,
  uint16_t wLength);

---
FX3 Firmware: Devices
  1. Example (based on dev-kit, general testing):
    1. SPI Flash (4 Mbit), GPIO toggle, static S/N setting
  2. Src_Sink (based on dev-kit, transfer testing):
    1. SPI Flash (4 Mbit), DMA overrides, MS Feature Descriptor
  3. SBRet10FX3 (based on data-sheets for new board):
    1. SPI Flash (8 Mbit), SPI FPGA (Lattice ECP3-17), I2C (IMU access),
      GPIO (controls, LED), S/N setting from Flash (init),
      FPGA configuration from Flash (init), FPGA configuration while
      running (vendor requests), MS Feature Descriptor

---
FX3 jAER integration
  - PROOF OF CONCEPT ONLY, soon to be deprecated!
  - New HardwareInterface package: cypressfx3
  - New Chip package: retina3
  - Code clean-up, re-factoring
  - Uses Thesycon USBIO library for easy USB communication
    1. v 2.71.0 (14.11.2012) used
    2. “The USBIO driver is designed to support
      USB 3.0 devices with super speed“
      (Thesycon Manual v 2.71.0)

---
Done!
  Thanks for your attention!
  Any questions?